## Slide 1
IP
header
IPsec
header
Secure
payload
IP
header
IPsec
header
Secure
payload
IP
header
IPsec
header
Secure
payload
IP
header
payload
IP
header
payload
headquarters
branch office
salesperson in hotel
laptop
w/ IPsec
router w/
IPv4 and IPsec
router w/
IPv4 and IPsec
public Internet
Virtual Private Networks (VPNs)

## Slide 2: Two IPsec protocols
Authentication Header (AH) protocol
  provides source authentication & data integrity but not confidentiality
Encapsulation Security Protocol (ESP)
  provides source authentication, data integrity, and confidentiality
  more widely used than AH

## Slide 3: Four combinations are possible!
Host mode with AH | Host mode with ESP
Tunnel mode with AH | Tunnel mode with ESP
most common and most important

## Slide 4: Security associations (SAs)
before sending data, “security association (SA)” established from sending to receiving entity
  SAs are simplex: for only one direction
ending, receiving entitles maintain state information about SA
  recall: TCP endpoints also maintain state info
  IP is connectionless; IPsec is connection-oriented!
how many SAs in VPN w/ headquarters, branch office, and n traveling salespeople?

## Slide 5: Example SA from R1 to R2
R1 stores for SA:
32-bit SA identifier: Security Parameter Index (SPI)
origin SA interface (200.168.1.100)
destination SA interface (193.68.2.23)
type of encryption used (e.g., 3DES with CBC)
encryption key
type of integrity check used (e.g., HMAC with MD5)
authentication key
193.68.2.23
200.168.1.100
172.16.1/24
172.16.2/24
security association
Internet
headquarters
branch office
R1
R2

## Slide 6
Security Association Database (SAD)
endpoint holds SA state in security association database (SAD), where it can locate them during processing.
with n salespersons, 2 + 2n SAs in R1’s SAD
when sending IPsec datagram, R1 accesses SAD to determine how to process datagram.
when IPsec datagram arrives to R2, R2 examines SPI in IPsec datagram, indexes SAD with SPI, and processes datagram accordingly.